Coefficients from Properties
Suppose there is a data set that forms a curve with three critical points and a shape that is consistent with a curve given by a degree four polynomial. From just these three critical points, it is possible to find all of the coefficients of said polynomial, henceforth denoted as ‘f’.
Let f:setR toward setR be defined as f( x`;`a,b,c,d,e )`def`ax^4+bx^3+cx^2+dx+e , where a`<>`0 .
g( x )`def`{ %delta f } over { %delta x }`=`4ax^3+3bx^2+2cx+d newline h( x )`def`{ %delta g } over { %delta x } `=` 12ax^2+6bx+2c newline r( x )`def`{ %delta h } over { %delta x }`=`24ax+6b
The roots of ‘g’ are equal to the x-coordinates of the critical points of ‘f’ and the roots of ‘h’ are equal to the x-coordinates of the inflection points of ‘f’.
To solve for ‘b’ in terms of ‘a’ first note that x-coordinate of the extremum of ‘h’ is at the center of the two inflection points of ‘f’.
Ex_x( h )`=`{ IP_0x + IP_1x } over 2
And the x-coordinate of the extremum of ‘h’ is equal to the root of ‘r’.
r( Ex_x(h) )`=`0
Which makes it possible to solve for ‘b’ in terms of ‘a’.
24aEx_x( h )+6b`=`0 newline newline bold {b `=` -4aEx_x( h )`=`-2a(IP_0x + IP_1x)}
Next, solve for ‘c’ in terms of ‘a’.
h( ip_x )`=`0 , where ip_x in lbrace IP_0x, IP_1x rbrace .
12aIP_0x^2+6bIP_0x+c`=`0 newline c `=` -( 12aIP_0x^2 -12a(IP_0x + IP_1x)IP_0x ) newline newline bold { c `=` 12 ` cdot ` a ` cdot ` IP_0x ` cdot ` IP_1x }
To solve for ‘d’ in terms of ‘a’:
g( cp_x )`=`0 where cp_x in CP_x and CP_x denotes the set of critical points of ‘f’ ordered under magnitude – i.e. CP_0x < CP_1x < CP_2x .
4aCP_2x^3 + 3bCP_2x^2 + 2cCP_2x + d `=` 0 newline newline d `=` -( 4aCP_2x^3 - 6a(IP_0x + IP_1x)CP_2x^2 + 24aIP_0x IP_1x CP_2x ) newline newline bold { d `=` -2a(2CP_2x^3 - 3(IP_0x + IP_1x)CP_2x^2 + 12IP_0x IP_1x CP_2x ) }
Finally, solve for ‘e’ in terms of ‘a’.
f( IP_0x )`=`IP_0y newline e `=`IP_0y -( aIP_0x^4 + bIP_0x^3 + cIP_0x^2 + dIP_0x) newline newline e `=` IP_0y - ( aIP_0x^4 -2a(IP_0x+IP_1x)IP_0x^3 + 12aIP_0x^3 IP_1x + dIP_0x) newline bold { e `=` IP_0y - (10aIP_0x^3 IP_1x ` - ` aIP_0x^4 + dIP_0x) }
Which makes it possible to solve for ‘a’.
f( CP_0x )`=`CP_0y newline aCP_0x^4 - 2a( IP_0x + IP_1x )CP_0x^3 + 12aIP_0x IP_1x CP_0x^2 + dCP_0x + e `=` CP_0y newline newline CP_0y - IP_0y`=` aCP_0x^4 - 2a( IP_0x + IP_1x )CP_0x^3 + 12aIP_0x IP_1x CP_0x^2 newline -2a(2CP_2x^3 - 3(IP_0x + IP_1x)CP_2x^2 + 12IP_0x IP_1x CP_2x )(CP_0x - IP_0x) newline -10aIP_0x^3 + aIP_0x^4

It is now possible to find the value of all of the other coefficients of ‘f’ since they are in terms of ‘a’.